## Slide 1: Robotic Indoor Localization using IMUs
Group No: 50 Date: 05/05/2016
Team Members
Project Advisor (Guide) : Dr. Vidhya Balasubramanian
S.No | Reg.No | Name | Section
1 | CB.EN.U4CSE12123 | Kiran Kassyap S | CSE-B
2 | CB.EN.U4CSE12144 | Srivenkata Krishnan | CSE-B
3 | CB.EN.U4CSE12147 | Sundarrajan G | CSE-B

## Slide 2
ROBOTIC INDOOR LOCALIZATION
USING INERTIAL MEASUREMENT UNIT

## Slide 3
PROBLEM STATEMENT
To develop an error reducing algorithm for Indoor localization of mobile robots using
the inertial measurement units(IMUs) and
Range finder sensors.

## Slide 4
PREVIOUS IMPLEMENTATION
Implemented the obstacle avoidance system and have made the robot autonomous
Obtained orientation from range finder sensors and position was estimated

## Slide 5
WORK IMPLEMENTED
Integrated three position values with help of a complementary filter to obtain accurate position of the robot
The three positions are as follows:
Position estimated from motor encoders[1]
Position obtained from gyroscope
Position calculated from range finder sensors[2]

## Slide 6
COMPLEMENTARY FILTER
angle = (1-alpha)*(gyro_angle) + (alpha)*(obstacle)
Alpha value is calculated with help of number of obstacles present in the environment
The more the obstacles the more the alpha value.
Alpha value is always less than 1.

## Slide 7
EXPERIMENTS UNDERTAKEN
SQUARE TRAJECTORY
EIGHT TRAJECTORY
RANDOM TRAJECTORY

## Slide 8
SQUARE TRAJECTORY

## Slide 9
EIGHT TRAJECTORY

## Slide 10
RANDOM TRAJECTORY

## Slide 11
Methods implemented | Trajectory 1 (Square) (cm) | Trajectory 2 (Eight) (cm) | Trajectory 3 (Random) (cm)
Encoders | 121.96 | 89.27 | 333.65
Gyroscope | 40.50 | 44.22 | 75.33
CDA_nO | 28.64 | 39.50 | 65.38
CDA_O | 20.25 | 34.68 | 20.49
AVERAGE EUCLEDEAN ERROR

## Slide 12
APPLICATIONS
Can be used as assistive robots in emergency situations which can be hazardous to humans

## Slide 13
[1] Dominik Gusenbauer, Carsten Isert and Jens Krösche, “Self-Contained Indoor Positioning on Off-The-Shelf Mobile Devices”, International Conference on Indoor Positioning and Indoor Navigation (IPIN), 15-17 September 2010.
[2] Robot pose correction using photogrammetric tracking", Proc. SPIE 4189, Machine Vision and Three-Dimensional Imaging Systems for Inspection and Metrology, 170 (February 12, 2001)
REFERENCE